ArdiChef Project
The Automated Kitchen Cooker

Started By: Thomas G (12/2014)
Feel free to use: no strings attached (text content only / images respectfully referenced)

# INTRODUCTION
The ArdiChef project will reside within http://www.github.com/tgit23/ArdiChef/
## Software
The software will mostly be written using the Arduino programming software package along with the "Processing" programming language.
## Control
The ArdiChef project will be controlled using the Arduino project (http://www.arduino.cc/) micro-controller board and mimic a lot of the 3D RepRap printer project technologies.
## Hardware
- Repository of Models	- http://www.github.com/tgit23/Ardichef/ → Hardware/
- Bill of Materials
Many of the hardware parts are printed using a 3D printer while some will need to be purchased. Currently all 3D printed parts are designed in Google Sketchup and stored at
# FOOD DISPENSERS
## Granular Foods Dispenser (GFD-28BYJ)
Granular foods like sugars and spices can be dispensed using what I'd call the Gumball approach. A circular plate with holes in it rotating to a covered drop-hole.
### 1-Gallon Can Granular Foods Dispenser (GC-GFD-28BYJ)

The 1-Gallon granular food dispenser requires
- One Gallon Tin Can with a base diameter that measures 16.125 inches
- 28BYJ-48 5Vdc 4-Phase 5-Line Stepper Motor with ULN2003 Driver Module Board
- 3D Printer for printing the following parts @ http://www.github.com/tgit23/ArdiChef → /Hardware/GranularDispensers

File-Name	Google Sketchup	Thumb	Description
MotorMount.skp	2014 - Inches		1) The 28BYJ Stepper motor is bolted into this motor mount (Shaft up)
DispGear_4inHoles.skp	2014 -Inches		2) The Disp (Dispense) gear is placed on the motor shaft
GallonCanBase_6pt125inchBase.skp	2014 - Inches		3) The “MotorMount/Stepper/DispGear” assembly is then bolted to the CanBase / 4) The Assembly is then attached to the bottom of the One-Gallon tin can.
MotorMountSpout.skp	2014 - Inches		5) Optionally – A spout holder can be attached to the MotorMount under the dispensing hole.

## Powder Foods Dispenser (PFD-28BYJ)
### 1-Gallon Can Powder Foods Dispenser (GC-PFD-28BYJ)
The 1-Gallon powder food dispenser requires
- One Gallon Tin Can with a base diameter that measures 16.125 inches
- 28BYJ-48 5Vdc 4-Phase 5-Line Stepper Motor with ULN2003 Driver Module Board
- 3/4” Shedule 80 PVC Pipe threaded and notched the height of the tin can
- 3/4” PVC Pipe Nut (Created by cutting a PVC cap)
- 3D Printer for printing the following parts

File-Name	Google Sketchup	Thumb	Description
MotorMountGearBox.skp	2014 - Inches		1) The 28BYJ Stepper motor is bolted into this motor mount gear box (Shaft up)
MotorGear.skp	2014 -Inches		2) The MotorGear is placed on the motor shaft
PipeDriverGear.skp	2014 - Inches		3) The PipeDriverGear is dropped freely into the MotorMountGearBox.
Scrapper.skp	2014 - Inches		5) The Scrapper is attached (glued) to the top of the 3/4” Threaded and notched PVC pipe.
GalCanBase_ThreeQtrNutBase.skp			6) The PVC Nut is glued into the CanBase / 8) The CanBase is then attached to the bottom of a one-gallon tin can / 9) The “MotorMountGearBox/MotorGear/PipeDriverGear” assembly is bolted to the CanBase. / 10) The Threaded and Notched “PVC-Pipe/Scrapper” is threaded down the CanBase till the PipeDriverGear's Notches catches the Notches in the PVC pipe.

T

# Up For Discussion
1. 4- Canisters into one spout or 4-spouts together
2. Turn-table or Conveyor
3. Mixer on mixing bowl over head?

# Bill Of Materials (BOM)
## Tools
- 3D Printer
- Pipe Threader Die for 1/2” and 3/4” pipes
## Materials
- 1/2” Schedule 80 PVC Pipe
- 3/4” Schedule 80 PVC Pipe
## Original Purchases

Qty/SKU/Price	Product Name / Description	Picture
(2) / 106842801 / $30.54 / www.gearbest.com	GZGW09 3D Printer Reprap Stepper Motor Driver Module Works with Official Arduino / GZGW09 3D Printer Reprap Stepper Motor Driver Module / Step angle: 1.8 degree Rated voltage: DC 4.83V Rated current: 0.84A Phase impedance: 5.75 Ohm + / - 10 degree centigrade Phase inductance: 9.3 mH + / - 20 degree centigrade (1kHz 1V RMA) Shaft diameter: 5mm / 0.188 Shaft length: 20mm Motor height: 34mm Number of lead wire: 4 wires / Product Weight: 0.22 kg Package Weight: 0.23 kg Product Size(L x W x H): 5.8 x 4.2 x 4.2 cm / 2.28 x 1.65 x 1.65 inches Package Size(L x W x H): 8.0 x 6.0 x 5.0 cm
(3) / NZ0019501 / $11.22 / www.gearbest.com	28BYJ-48 5V 4-Phase 5-Line Stepper Motor with ULN2003 Driver Module Board / Google Sketchup 3" x 5 3/16" Rectangular Drive Hole
(2) / NZ0049801 / $75.24 / www.gearbest.com	Arduino MEGA2560 RepRap Circuit Sets for 3D Printer Ramps / Package Contents: / 1 x MEGA2560 Circuit Sets / 1 x Ramps 1.4 / 4 x A4988 / 1 x USB Cable
(1) / 277147 / $4.99 / www.dx.com	Double Tip 21cm Dupont Cable - Black + Multicolored (70 PCS)
(1) / 145357 / $7.91 / www.dx.com	3-Pin Power Adapter Socket with Rock Switch for DIY Project - Black + Red (5-Piece Pack)
(1) / 344826 / $4.80 / www.dx.com	S401 1/4" Water Flow Sensor for Dispenser / Coffee Machine - White
(1) / 263660 / $10.99 / www.dx.com	DIY Copper Breadboard DuPont Connection / Test Cables - Multicolored (200 PCS)
(1) / 123648 / $1.46 / www.dx.com	2.54mm Mini Jumper Connector - Black (50-Piece Pack)
(1) / 162180 / $3.91 / www.dx.com	1-Pin Female to Female DuPont Cables for Arduino (2 x 40 PCS / 21cm)
(1) / 206265 / $1.77 / www.dx.com	SZF303 Small Water Pump Motor Water / Oxygen Pipe / Tube - Transparent (100cm) / Model SZF303 / Quantity 1 / Color Transparent / Material Plastic housing / Features Use for small fish tank oxygen supply; DIY project / Specification Inner diameter: 0.2cm; Thickness: 0.4cm; Length: 100cm / Application Small water pump pipe / tube / English Manual/Spec No / Packing List 1 x Water pipe / Dimensions: 39.37 in x 0.16 in x 0.16 in (100.0 cm x 0.4 cm x 0.4 cm) / Weight: 0.32 oz (9 g)
(1) / 232242 / $2.41 / www.dx.com	DIY Plastic Water Pump Line Tube - White (4 PCS) / Brand N/A / Quantity 4 Piece(s)/pack / Color White / Material Plastic / Compatible Models Small water pump / Application Used to connect small water pump / Other Feature Outer diameter: 4mm; Inner diameter: 3mm / Packing List 4 x Water pump line tubes / Dimensions: 1.14 in x 0.71 in x 0.16 in (2.9 cm x 1.8 cm x 0.4 cm) / Weight: 0.18 oz (5 g)
(1) / 203330 / $4.99 / www.dx.com	20904 Silicone Tube Pipe - Translucent White (5 Meters) / Model 20904 / Quantity 1 / Color Translucent white / Material Silicone / Specification Outer diameter: 5mm; Inner diameter: 3mm; Thickness: 12mm; Working temperature range: -65'C~200'C / Features Silicone tube / Application Widely used for water dispenser, coffeemaker, electronic instrument, medical equipment, wine connection tube etc. / English Manual/Spec No / Packing List 1 x Silicone tube (5 meters) / Dimensions: 196.85 in x 0.20 in x 0.20 in (500.0 cm x 0.5 cm x 0.5 cm) / Weight: 2.82 oz (80 g)
(2) / 236808 / $5.23 / www.dx.com	HSYY01 Micro Gear Water Pump Motor w/ Hose - White + Silver / $5.23 / Brand N/A / Model HSYY01 / Quantity 1 / Color White + Silver / Material Iron casing + PVC / Specification Working voltage: 4~12V; Working current: 0.8A; / Motor diameter: 2.7cm; inlet opening outer diameter: 0.4cm Features Working voltage: 4~12V; Working current: 0.8A; / Motor diameter: 2.7cm; inlet opening outer diameter: 0.4c. / Water flow rate: Approx. 1.2L/M (5V) / Application DIY project / English Manual/Spec NO / Packing List / 1 x Motor 1 x Hose (100cm) / Dimensions: 2.56 in x 1.69 in x 1.61 in (6.5 cm x 4.3 cm x 4.1 cm) Weight: 3.03 oz (86 g)
(1) / 229082 / $5.92 / www.dx.com	DIY Electric Motor Mini Water Pump / $5.92 / Brand N/A / Quantity 1 Piece(s)/pack / Color Silver + white / Material Iron + copper + plastic / Compatible Models N/A / Application Testing, fish-farming, etc. / Other Feature Inlet and outlet hole external diameter: 4mm; Rated voltage: 7.2V; DC voltage: 3~9V; Please note: No-load test should not take a long time; With plastic blade, Can't be inhaled impurities / Packing List 1 x Pump / Dimensions: 2.56 in x 1.61 in x 1.50 in (6.5 cm x 4.1 cm x 3.8 cm) / Weight: 2.54 oz (72 g)
(1) / 300904 / $8.48 / www.dx.com	5.5V- 12V Submersible Water Pump - Black / Voltage: 3.5-12V, head: 40-160cm. the maximum flow: 300L/H. 60 degrees below temperature resistant. - Continuous working life (24 hours non-stop work) more than 20000 hours, about 10 hours per day, water pump life for 8 years. - The inlet and outlet diameter is 8.3MM, the inner diameter 6.2MM. With 2 soft sucker, can be fixed freely. - Super mute, noise figure is 30dB / Brand: N/A / Quantity: 1-Piece / Color: Black / Material: ABS / Dimensions: 1.89 in x 1.57 in x 1.06 in (4.8 cm x 4 cm x 2.7 cm) / Weight: 2.52 oz (71.5 g) / Packing List: 1 x Pump (38cm-cable)
(1) / 185970 / $6.49 / www.dx.com	MPX08 Micro Liquid Gear Pump w/ Silicone Tube - White (DC 5V) / Model MPX08 / Quantity 1 / Color White / Material Plastic + Iron / Features Start current: 2A; Perfect for DIY projects such as fish tank, model, etc. / Packing List 1 x Micro pump / 1 x Silicone tube (100cm) / Dimensions: 2.56 in x 1.65 in x 1.54 in (6.5 cm x 4.2 cm x 3.9 cm) / Weight: 3.28 oz (93 g)

# Failed Attempts For Reference
## Powder Dispensing
Dispensing powder proved to be quite challenging
- Large holed Granular type approach – FAILED
- Funnel container – FAILED (Didn't attempt a super-long auger approach as it was thought to fail also)
- Large bottom “Water Wheel” type approach - FAILED
- Partial Solution “Top Down” – WORKS (But needs refinement – as per actual unit)
  - Creating a scrapper that falls down as product is removed while scrapping product to a center drop hole.
  - While this worked for flour – corn starch and small holed center (1/2” pipe) will most likely still be an issue
  - Disadvantages
    - The scrapping gear must be held up while filling the cannister
    - The center shaft has large holes that leak while filling the cannister
    - A cap must be put on the end of the shaft to keep it from binding the gear
    - Filling with flour is more difficult due to motor being attached at the top
    - The flour did dispense well as shown above the can has been dispensed of flour completely without any intervention.